## Slide 1: The ELT Primary Mirror Cyber-Security Workshop
Notes: The European Southern Observatory is building [in Chile, in the Atacama desert, on Cerro Armazones at 3000m elevation] a new [optical] telescope: the Extremely Large Telescope (ELT).
This presentation is about the local control SW of a subsystem of this telescope: the primary mirror.

## Slide 2
Name: Extremely Large Telescope (ELT)
Location: Cerro Armazones (3046m), Atacama Desert, Chile
First Light: 2029
Cost: 1.4 Billion EUR

## Slide 3
The primary mirror (M1) of ESO’s Extremely Large Telescope has a diameter of 39 m

## Slide 5: M1 Segments
Segments are organized in flowers of up to 7 segments
Each flower is controlled by 1 Segment Concentrator Cabinet (SegC) for a total of 132 cabinets (PLC, PSU, Control Modules, Network Switch)
In addition, there are 6 Sector Distribution Cabinets (PLC, PSU)

## Slide 6: Network Layout
Sector Switch (sector 1 of 6)
Sector Switch (sector 1 of 6)
Sector Switch (sector 6 of 6)
Sector Switch (sector 6 of 6)
SegC Switch (1 of 132)
SegC Switch (2 of 132)
SegC Switch (22 of 132)
SegC Switch (21 of 132)
SegC Switch (112 of 132)
SegC Switch (113 of 132)
SegC Switch (132 of 132)
SegC Switch (131 of 132)
CR Switch
CR Switch
...
...
...
...
...
...
...
...
Computer Room
M1 cell
M1LCU(s)
10 GigB Ethernet
100 MegB Ethernet
1 GigB Ethernet

## Slide 7: System Stack
Linux with RT profile
GNU C++, Python
ZMQ, FastDDS, OPCUA, SNMP
Redis, Nomad, Consul
RAD: Rapid Application Framework based on interpreted State Machines (SCXML)
GUI: Qt + Taurus
SW Stack

## Slide 8: SW Installation & Deployment
Installation using Ansible scripts:
  RPMs installation
  User environment config.
  Server RT properties (core isolations, etc.) config.
  Nomad/Consul services config.
  Time service config. (PTP)
  Network config. (NIC)
  Other services configs. (shared volumes)
Deployment using Nomad/Consul:
  Start/Stop applications on remote servers
  Reserve static IP/port assignment
  Remote monitoring
  Periodic health check
  Auto-restart

## Slide 9: Remote Access / Remote Engineering Data Access
Remote Access (ELT):
  Requires special approval
  Not defined yet the technology
Remote Access (VLT):
  Requires special approval
  Only from dedicated ESO offices
  A person must supervise the remote session at the Observatory
  Using VNC:
    Observatory starts VNC server
    VNC client connects
Remote Eng. Data Access (ELT):
  TBD
Remote Eng. Data Access (VLT):
  Via a dedicated “bridge” server which allows using SFTP to:
    write/read the data to/from the “bridge” server from outside the control network
    write/read the data to/from the “bridge” server from within the control network